## Slide 1
Enviro Loo Clear Non-Sewered Sanitation System [Water Efficient Solution]

## Slide 2
The Enviro Loo Clear NSSS is an outcome of the Bill & Melinda Gates Foundation’s [BMGF] funded reinvent the toilet challenge launched during 2011.
Through the Water Research Commission’s [WRC] South African Sanitation Technology Enterprise Programme [SASTEP], Enviro Options were asked to evaluate the technology to apply it in the African continent.
The evaluation process started during August 2020.
Additionally, we obtained an exclusive manufacturing licence from IP Developer and Owner.
Enviro Options Pty Ltd are the first Company to manufacture and market this product on the African Continent.
To date 10 x complete pilot projects were successfully implemented & well accepted in South Africa since August 2020.
The 1st commercial off-grid project was commissioned in February 2023, at Ethembeni Primary School in Mpumalanga
BACKGROUND OF THE ENVIRO LOO CLEAR NON-SEWERED SANITATION SYSTEM

## Slide 3
“Off the grid” Non-Sewered [Closed-Loop] Sanitation Solution that uses a completely natural biological process to treat wastewater and kill pathogens and recycle for flushing.
The system is a sealed prefabricated integrated treatment unit [category D of DWS standards i.e.; requiring no licenses & permits, comprising Control Room – fully automated with PLC & EDB, requiring initial non-potable water loading;
No need for chemicals, municipal sewer connections and bulk treatment plants or continuous water supply.
PROPOSED SOLUTION DESCRIPTION
T6 & T24 MODELS

## Slide 4
From the front-end the waste is moved to the wastewater treatment system where it is treated with a physical precipitation in an aerobic reactor.
Any foreign objects i.e.; sanitary pads that are flushed away through into the system, will be shredded by an improved macerater pump fitted into the collection tank.
Bacteria introduced into the aerobic reactor attaches itself to the waste as biofilm. The biofilm biodegrades the organic pollutants and reduces their concentration.
The wastewater is then treated within a MBR (membrane biological reactor) which separates the pollutants.
The treated water is further disinfected via an ozonating process and the treated water is recirculated for the next flush.
New / Existing Frontend Ablutions
TANK 1
under ground
TANK 2
above ground
TANK 3
above ground
TANK 4
above ground
Backend
Frontend
HOW IT WORKS
Frontend
Backend

## Slide 5
Transforms the lives of individuals, as well as empowering communities, by providing a fully recycling and aspirational quality flushing toilet experience through a cost effective, sustainable, and dignified sanitation system.
  T6 – daily treatment capacity of 6KL per day, which can be connected to +/- 50 seats;
  T24 – daily treatment capacity of 24KL per day; which can be connected to +/- 200 seats;
SCALABILITY -
Increase / Decrease
ADAPTABILITY
  Ability to relocate or decommission installed solution/s if required;
  Geared for deployment for various project applications i.e., Schools or Category A, B1 and C informal settlements and / or areas with little or no access to adequate sanitation and bulk infrastructure;
  Can be connected to existing or new single household and communal frontend ablution facilities.
  Can be set to 8 bar-pressure for long distance or uphill in between backend & frontend.
ENVIRONMETAL
EFFICIENCY
  The self-contained treatment plant prevents the illegal disposal of waste into the environment and can be located near to classrooms or homesteads ensuring safety of people; ZERO DISCHARGE.
  Water saving – initial maximum non-potable water loading;
  Solar powered or connected to electrical mains requiring 220 volts, 60 Amp single phase mains, part backup solar or full solar at 7.2KW.
BENEFITS & ADVANTAGES

## Slide 6
ENVIRONMETAL
EFFICIENCY
BENEFITS & ADVANTAGES CONTINUES…
ENVIRONMENTAL EFFICIENCY Continues…
Site footprint for T6 (6,000 litres) is 8 meters x 10 meters on 150 millimetres supporting concrete plinth site dependent.
RELIABILITY
Technology Readiness Level (TRL) 9 : System demonstrated, tried & tested and ready for use;
AFFORDABILITY
No need for continuous water supply or sewer connections;
System evaluated through Water Research Commission of South Africa under “South African Sanitation Technology Enterprise Programme” (SASTEP).
Operating off grid;
Site footprint for T24 (24,000 litres) is 8 meters x 15 meters on 150 millimetres supporting concrete plinth site dependent.
No chemicals required for maintenance;
ISO 30500 Standards for system performance and ISO 9001:2015 Quality Management Systems
Affordable Capex & Opex.

## Slide 7
Minor service – Membrane clean every six [6] to ten [10] months. No loss of water with a downtime of 8 hours. Planned and scheduled.
Major service – de-sludge tanks [primary, anoxic, aeration and membrane] cleaned every eighteen [18] to twenty-four [24] months. Non-Portable Water reloading at +/- 18,000 litres required with a downtime of 48 hours. Planned and scheduled.
Sludge is treated onsite via a sludge digester/autoclave and safely transported and disposed of offsite as per local authority regulations.
BUSINESS MODEL / VALUE PROPOSITION:
Replicate the existing Enviro Options business model of appointing locally based, trained, accredited servicing and maintenance technicians / SMME’s.
This aligns to the company’s ethos of socio-economic development, job creation, local economic development and providing a cost-efficient national service platform.
Alternatively, as in the case with Johannesburg Water, full Technology Transfer.
100% availability of parts and replacement equipment locally.
MAINTENANCE PROCESS AND SITE LAYOUT DRAWINGS

## Slide 8
TYPICAL INSTALLATIONS

## Slide 9
THANK YOU
Thapelo Makwela
Business Development Manager
Tel: +27(0) 11 762 1624
Cell: +27(0) 71 609 9533
Email: info@enviroloo.co.za OR
thapelo.makwela@enviro-loo.com
Address: |27 Pillans Street | Chamdor | Krugersdorp |
|Gauteng|
The Enviro Loo Clear NSSS Plant takes alternative sanitation to the next level of innovation!!!